## Slide 1
Understanding transmon qubits : hardware, dynamics and pulse caliberation
Three-level transmon physics ,Hamiltonian modelling, and adaptive caliberation
Background • Physics • Python code • Calibration policies • Downstream algorithm
Q-BLUEPRINT PROJECT EXPLAINER

## Slide 2
The story of the project in one picture
02
1. The device drifts
A transmon's effective frequency and pulse response can slowly change during operation.
2. Gates become imperfect
The same control pulse may rotate the qubit by the wrong angle or create leakage.
3. We recalibrate
Use measurements to estimate amplitude, frequency, and DRAG β.
4. Test the impact
Run a QAOA MaxCut computation and compare its cost under each policy.
Core question: how do we keep gates accurate without wasting the whole day calibrating?
This is a control-and-optimisation problem: measure the device, update our settings, and quantify the benefit.

## Slide 3
BACKGROUND
Why does quantum-gate accuracy matter?
03
A qubit
A two-level quantum system with basis states |0⟩ and |1⟩.
A gate changes its quantum state. For example, an X-like π pulse swaps |0⟩ and |1⟩.
A physical qubit
A real transmon is not a perfect two-level system. It has levels |0⟩, |1⟩, |2⟩, …
We use |0⟩ and |1⟩ as the computational qubit, but control pulses can accidentally populate |2⟩.
A calibration
Calibration finds control settings that make the intended operation happen as accurately as possible.
It is like tuning a musical instrument before playing a precise piece.
Small errors can accumulate across many gates, so a tiny calibration improvement can matter to an algorithm.

## Slide 4
PHYSICS BASICS
What is a transmon, and why use three levels?
04
A transmon is a superconducting circuit used as a qubit. Its lowest energy levels are not equally spaced.
Energy
|2⟩ leakage level
|1⟩ excited qubit state
|0⟩ ground state
The |1⟩→|2⟩ transition has a different frequency from |0⟩→|1⟩. This anharmonicity helps address the qubit transition selectively.
Why model |2⟩?
To measure leakage rather than pretending it cannot happen.

## Slide 5
PHYSICS BASICS
How does a pulse rotate a qubit?
05
Control amplitude
The drive amplitude sets how strongly the microwave pulse acts. Too small → under-rotation; too large → over-rotation.
Drive frequency / detuning
Detuning is the difference between the applied drive frequency and the qubit transition frequency. Nonzero detuning changes the rotation axis and can reduce gate fidelity.
A_pulse = amp * A
Ωx(t) = A_pulse · exp[-(t − t₀)² / (2σ²)]
Ωx,detuned(t) = Ωx(t) · cos(Δ t)
Δ = drive frequency − qubit frequency
The exact convention depends on the rotating-frame Hamiltonian used in the simulator; the key idea is that detuning changes the effective drive dynamics.

## Slide 6
PHYSICS BASICS
Gaussian pulses and leakage
06
A Gaussian pulse turns the drive on and off smoothly instead of switching abruptly.
time →
Desired action
A calibrated Gaussian π pulse should rotate |0⟩ to |1⟩.
Unwanted action
Strong or poorly shaped pulses can also drive population into |2⟩.
Leakage is population outside the computational subspace: approximately P₂ for this three-level model.

## Slide 7
PHYSICS BASICS
What is DRAG, and what does β do?
07
Problem
A fast pulse can unintentionally excite |1⟩→|2⟩ and add phase errors.
DRAG idea
Add a carefully chosen quadrature component related to the time derivative of the main Gaussian envelope.
β (beta)
β controls the strength/sign of this correction. DRAG calibration searches for the β that minimises leakage and gate error.
Ωy(t) ∝ β · dΩx(t)/dt
Exact signs and scaling depend on the Hamiltonian convention; think of β as the knob controlling the correction pulse.

## Slide 8
PYTHON CODE
Reading the simulator: what does simulate_pulse do?
08
def simulate_pulse(amp, beta=0.0, detuning=0.0):
A_pulse = amp * A
def omega_x(t, args):
t0 = T_gate / 2
return A_pulse * exp(-((t-t0)**2)/(2*sigma**2)) * cos(detuning*t)
def omega_y(t, args):
# DRAG correction
return beta * derivative_of_gaussian(t)
H_tot = [H0, [Hd, omega_x], [H_drag, omega_y]]
res = mesolve(H_tot, psi0, tlist, e_ops=projectors)
return P0, P1, P2, final_state
Inputs
amp, β and detuning
Inside
Build time-dependent Hamiltonian and solve Schrödinger / master-equation dynamics.
Outputs
Final populations P₀, P₁, P₂ and the final state vector.
This is a schematic reading guide, not a guaranteed line-for-line copy of the notebook.

## Slide 9
PYTHON CODE
What does self.run_experiment(...) do?
09
It is a wrapper that runs a pulse experiment and turns the simulator result into a measurement-like result.
p1, other_result, shots = self.run_experiment(
lambda: self.sim_func(amp=amp),
shots_per_point
)
• lambda: ... supplies the experiment to execute; it lets the wrapper call it when needed.
• self.sim_func(amp=amp) simulates the pulse at the current candidate amplitude.
• shots_per_point is the number of repeated measurement trials at this setting.
• The wrapper typically returns an estimated outcome probability, any extra result, and the number of shots used.
Important: the exact meaning of the second return value depends on your run_experiment definition.

## Slide 10
CALIBRATION
Task 2(a): calibrating the π-pulse amplitude
10
Goal: find the amplitude that gives the desired π rotation, ideally moving |0⟩ → |1⟩.
1. Coarse scan
Try a range of amplitudes, for example 0 to 2, and measure P₁ for each.
2. Fine scan
Focus on the best region. Error amplification (e.g. repeated pulses) makes small amplitude errors easier to detect.
3. Choose
Select the amplitude with the largest measured P₁, while checking leakage and uncertainty.
amps = np.linspace(0.0, 2.0, 21)
for amp in amps:
p1, _, shots = run_experiment(...)
p1_measured.append(p1)
optimal_amp = amps[np.argmax(p1_measured)]

## Slide 11
CALIBRATION
Task 2(b): frequency calibration with Ramsey
11
Ramsey converts a frequency mismatch into a measurable oscillation as we vary the free-precession delay τ.
Prepare superposition → wait τ → recombine / measure
P(1 | Δf, τ) = ½ [1 + cos(2π Δf τ)]
P(0 | Δf, τ) = 1 − P(1 | Δf, τ)
• Δf is the unknown frequency offset.
• Longer τ can make small offsets easier to see, but oscillations repeat (aliasing).
• The sign can be ambiguous from one delay alone; use multiple delays or a prior.
The Hadamard-like rotations prepare and read out interference; the waiting period lets the phase difference accumulate.

## Slide 12
ADAPTIVE CALIBRATION
Likelihood vs posterior: two different jobs
12
get_likelihood(outcome, τ, df_grid)
Question it answers:
“If the true detuning were each candidate value on df_grid, how likely is this observed 0 or 1?”
It evaluates the Ramsey probability for every candidate detuning and returns the probability of the observed outcome.
update_posterior(...)
Question it answers:
“After seeing this result, how plausible is each candidate detuning now?”
Bayes' rule multiplies prior belief by the likelihood and normalises the result.
posterior_new ∝ likelihood × posterior_old
posterior_new = posterior_new / sum(posterior_new)
Likelihood scores a possible explanation; posterior is our updated distribution over explanations.

## Slide 13
ADAPTIVE CALIBRATION
Why does select_next_tau choose a delay?
13
Instead of testing every delay in a dense grid, choose the next delay expected to teach us the most.
1. Current uncertainty
Calculate posterior entropy. A broad posterior means we are uncertain about detuning.
2. Try candidate τ
Predict the probability of outcomes 0 and 1 for each candidate delay, averaged over the current posterior.
3. Expected information gain
Estimate how much entropy should fall after the measurement. Pick the τ with the biggest expected reduction.
EIG(τ) = H(current posterior)
− expected H(posterior after outcome)
next_tau = candidate_taus[argmax(EIG)]
Adaptive calibration spends shots where they are most informative, rather than wasting shots uniformly.

## Slide 14
ADAPTIVE CALIBRATION
Task 3: how do we prove adaptive calibration helps?
14
• Start with a prior distribution over possible detunings.
• At each round, choose τ using select_next_tau().
• Generate a measurement outcome using the simulated true detuning and shot noise.
• Use the likelihood to update the posterior.
• Repeat; plot posterior narrowing and the selected sequence of delays.
• Compare precision versus total shots against a fixed dense-delay scan.
Posterior narrowing
The distribution concentrates around the true detuning.
Precision vs shots
How uncertainty decreases as measurement budget grows.
Shot saving
Shots saved = fixed-grid shots − adaptive shots at equal precision.

## Slide 15
POLICY LAYER
Task 4: compare three calibration policies
15
P0 · No recalibration
Calibrate once at the start, then keep using the same settings all day.
Cheap, but drift may make gates steadily worse.
P1 · Fixed schedule
Recalibrate at regular intervals.
Simple and predictable, but may calibrate when unnecessary or miss sudden drift.
P2 · Health check
Run a cheap check every few minutes; do a full calibration only when a statistic crosses a chosen threshold.
Can balance quality and overhead.
For each policy, record gate error over the simulated day—not just one final number.

## Slide 16
POLICY LAYER
What is drift in this project?
16
Drift means the device's effective control parameters change over time, even if the software settings stay fixed.
Frequency drift
The qubit transition frequency shifts, so the old drive is no longer perfectly on resonance.
Amplitude drift
The same command can produce a different rotation angle, causing under- or over-rotation.
Pulse-shape / β drift
The best DRAG correction may change, increasing leakage or phase error.
A policy is a rule for deciding when to spend time and shots checking or correcting these changes.

## Slide 17
EVALUATION
Task 5: Pareto analysis—quality versus overhead
17
Each policy trades off two goals:
A · Time-averaged gate error
How inaccurate were the gates, averaged across the simulated day? Lower is better.
B · Calibration fraction
What fraction of the day was spent calibrating rather than doing useful computation? Lower is better.
Pareto frontier
A policy is Pareto-dominated if another policy has both lower gate error and lower calibration overhead. Repeat with at least 20 drift seeds to show variability with error bars.

## Slide 18
DOWNSTREAM ALGORITHM
What is MaxCut, in simple words?
18
MaxCut divides the vertices of a graph into two groups so that as many edges as possible cross between the groups.
One cut: teal group vs coral group.
An edge counts if its endpoints are in different groups.
MaxCut is a useful benchmark optimisation problem: it lets us see whether imperfect quantum gates damage an algorithm's result.

## Slide 19
DOWNSTREAM ALGORITHM
How QAOA uses the quantum processor
19
1. Encode the problem
A cost Hamiltonian assigns better energy to bitstrings that cut more graph edges.
2. Apply a circuit
For p = 1, apply one cost layer and one mixing layer, controlled by angles often called γ and β (algorithmic β; distinct from DRAG β).
3. Measure and score
Measure bitstrings, compute their cut values, and estimate the expected cost. A classical optimiser can tune the angles.
Why connect it to calibration? Because every imperfect single-qubit gate can change the final bitstring distribution and reduce the achieved cut quality.

## Slide 20
DOWNSTREAM ALGORITHM
Task 6: how is an imperfect gate modelled?
20
The project asks us to build an effective 2 × 2 block M(t) from the transmon model and include rotation error, detuning error, and leakage.
ρ → MρM† + (1 − Tr[MρM†]) I/2
MρM†
The part that remains inside the computational qubit space after the imperfect operation.
Trace loss
If Tr[MρM†] is less than 1, some probability leaked out of the qubit subspace.
I/2 term
The given map redistributes lost probability as a maximally mixed qubit contribution, preserving total trace.
Two-qubit RZZ gates are assumed ideal in this task; the single-qubit gates carry the calibration-dependent error.

## Slide 21
RESULTS TO PRESENT
What does the final cost plot tell us?
21
Horizontal axis
Time of day. This reveals when drift begins to harm the computation and when recalibration occurs.
Vertical axis
Normalised cost ⟨C⟩/Cmax. It compares algorithm performance on a common scale.
Compare policies
A stronger policy should maintain better cost, but may spend more time calibrating. Report this trade-off, not just one winner.
Do not claim a policy wins before running the simulation: the plots and statistics must support the conclusion.

## Slide 22
CODE ROADMAP
Putting the Python pieces together
22
# 1. Simulate physical pulse dynamics
P0, P1, P2, psi_f = simulate_pulse(amp, beta, detuning)
# 2. Estimate an outcome using repeated shots
p1_hat, extra, shots = run_experiment(...)
# 3. Calibrate parameters
amp_hat = calibrate_pi_amplitude(...)
df_hat = calibrate_frequency_ramsey(...)
beta_hat = calibrate_drag(...)
# 4. Run policy through simulated day
trace = run_policy(policy, drift_seed=seed)
# 5. Evaluate downstream QAOA MaxCut
cost_trace = evaluate_qaoa(trace)
• Physics simulator: predicts the pulse dynamics.
• Measurement wrapper: adds shot noise and counts shots.
• Calibration routines: estimate control settings.
• Policy layer: decides when to recalibrate.
• Evaluation: measures gate error and algorithm cost.

## Slide 23
PRESENTATION NOTES
A simple way to explain the project aloud
23
“The project studies how to keep a superconducting transmon qubit calibrated while its parameters drift over time. We model three energy levels so that we can capture leakage into |2⟩. We first calibrate pulse amplitude, drive frequency, and the DRAG correction. For frequency calibration, Ramsey measurements provide information about detuning. Instead of testing all delays equally, Bayesian adaptive design selects the next delay expected to reduce uncertainty the most. We then compare three operating policies: no recalibration, fixed-schedule recalibration, and health-check-triggered recalibration. We measure both gate error and the time spent calibrating. Finally, we insert the resulting imperfect single-qubit gates into a p = 1 QAOA circuit for MaxCut on a four-qubit ring. This shows how hardware calibration choices can affect an actual quantum computation.”
Tip: explain the pipeline first; introduce equations only when someone asks how each stage works.

## Slide 24
REVISION
Quick glossary
24
Transmon
Superconducting circuit used as a qubit.
Detuning Δf
Difference between drive frequency and qubit transition frequency.
P₀, P₁, P₂
Populations in levels |0⟩, |1⟩ and |2⟩.
Leakage
Population leaving the computational |0⟩, |1⟩ space.
DRAG β
Knob setting the derivative-shaped quadrature correction.
Shot
One repeated prepare–operate–measure trial.
Likelihood
Probability of an observation under a candidate parameter.
Posterior
Updated probability distribution after observing data.
EIG
Expected information gain; predicted reduction in uncertainty.
Pareto frontier
Best trade-offs where no objective can improve without worsening another.

## Slide 25
TAKEAWAYS
The big picture: what should the project demonstrate?
25
• A three-level model captures both useful qubit rotation and leakage.
• Calibration estimates the settings that make gates more accurate.
• Bayesian adaptive Ramsey chooses informative delays and can reduce shot usage.
• Calibration policies trade gate quality against time spent recalibrating.
• The QAOA MaxCut test connects hardware-level errors to algorithm-level performance.
• Conclusions must be based on measured simulation results, with uncertainty across drift seeds.
Device physics → Calibration → Policy → Algorithm performance